## Slide 1: NKG geoid meeting, Copenhagen, Nov 2004
NKG-2004 Geoid Model
- most recent model -
R. Forsberg, G. Strykowski (KMS, Denmark)
M. Bilker (Finnish Geodetic Institute)

## Slide 2: Remove-restore principle
The anomalous gravity potential T is split into 3 parts:
T = TGGM02EGM + TRTM + Tres
TGGM02EGM – GRACE GGM02S global spherical harmonic model to 90
+ EGM96 beyond 100 (linear blending)
TRTM – Residual terrain effect (RTM)
Resolution: 42’ x 84’
Tres – Residual (i.e. unmodelled) regional/local gravity effect
To be computed by spherical FFT / Stokes

## Slide 3: Geoid and quasigeoid
Final goal is the geoid N, i.e. “inside masses” (H=0):
(T non-harmonic
inside masses)
Modelled directly: the quasi-geoid , i.e. “the geoid on topography”:
where  is the normal gravity,  is the latitude,  is the longitude and H is the (orthometric) height.

## Slide 4: Conversion from quasigeoid to geoid
Approximately, the relation between the geoid N and the quasi-geoid  is:
N- is the difference between the orthometric height
HP and the normal height H*P, gB is the Bouguer
anomaly and 0 is the normal gravity at the ellipsoid.
NKG2004 is basically a quasi-geoid!

## Slide 5: RTM terrain effects
Fourier-domain:

## Slide 6: Conversion of residual gravity (after RTM and EGM)
Stokes/Molodensky
where g1 is the first term in the Molodensky’s expansion
Stokes kernel

## Slide 7: Stokes kernel modification
Stokes’ kernel modification (i.e. modified Wong-Gore
method without ”sharp edges”):
where

## Slide 8: Gravity data used

## Slide 9: Compiled terrain data

## Slide 10: RTM reference topography

## Slide 11: Average classical terrain corrections from detailed DEMs
(converted to
RTM by Bouguer)

## Slide 12: Statistics of gravity data reductions
unit: mgal | mean | std.dev. | min. | max.
surface data (252856 pts) | 0.08 | 25.93 | -141.17 | 205.58
- GRACE/EGM | -0.90 | 21.63 | -164.21 | 155.56
- RTM | 0.71 | 16.69 | -97.98 | 132.38
airborne data (7869 pts) | -14.02 | 19.82 | -80.38 | 43.93
- GRACE/EGM | -0.67 | 13.97 | -43.31 | -47.79
- RTM | -0.17 | 13.80 | -40.96 | 49.46

## Slide 13: NKG2004 basic computations
Gridding by LSC and variable std.dev.(all <8mgal). Corr.length = 25 km, 2nd order Markov cov.fct.
FFT
Area: 53N-73N, 1E-33E
2000×1600 grid (100% zero padding)
Stokes function with and without modification (testing different solutions ..)

## Slide 14: Reduced gravity data

## Slide 15: Geoid effect from reduced gravity data

## Slide 16: RTM terrain effect

## Slide 17
Statistics of the restore step (example mod 30)
unit: m | mean | std.dev. | min. | max.
FFT quasi-geoid contribution from | 0.01 | 0.50 | -2.38 | 3.17
RTM terrain effect | 0.00 | 0.09 | -0.63 | 0.95
GRACE/EGM quasi-geoid | 30.65 | 10.52 | 14.08 | 49.36
Final quasi-geoid | 30.66 | 10.54 | 13.88 | 49.73

## Slide 18: Final geoid (mod 30)

## Slide 19: GPS-levelling comparisons (1)
Geoid – no mod Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.139 | 0.077 | 0.050
New Finnish GPS | 0.082 | 0.104 | 0.036
”Torge” | -0.036 | 0.098 | 0.042
SWET | -0.039 | 0.094 | 0.060
Baltic sea level | 0.072 | 0.016 | 0.064
REFDK | -0.207 | 0.038 | 0.021
Sognefjord | 0.077 | 0.069 | 0.063
New Norway GPS | -0.086 | 0.144 | 0.078
Geoid – mod 30 Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.558 | 0.067 | 0.040
New Finnish GPS | 0.390 | 0.037 | 0.032
”Torge” | 0.0385 | 0.151 | 0.041
SWET | 0.335 | 0.115 | 0.053
Baltic sea level | 0.438 | 0.094 | 0.067
REFDK | 0.149 | 0.041 | 0.020
Sognefjord | 0.451 | 0.072 | 0.063
New Norway GPS | 0.329 | 0.116 | 0.061

## Slide 20: GPS-levelling comparisons (2)
Geoid – mod 60 Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.557 | 0.070 | 0.049
New Finnish GPS | 0.416 | 0.056 | 0.045
”Torge” | 0.363 | 0.159 | 0.081
SWET | 0.336 | 0.087 | 0.053
Baltic sea level | 0.465 | 0.095 | 0.070
REFDK | 0.126 | 0.061 | 0.019
Sognefjord | 0.486 | 0.090 | 0.063
New Norway GPS | 0.299 | 0.101 | 0.066
Geoid – mod 90 Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.541 | 0.083 | 0.049
New Finnish GPS | 0.407 | 0.064 | 0.055
”Torge” | 0.362 | 0.202 | 0.102
SWET | 0.314 | 0.083 | 0.039
Baltic sea level | 0.480 | 0.105 | 0.083
REFDK | 0.122 | 0.063 | 0.034
Sognefjord | 0.456 | 0.107 | 0.064
New Norway GPS | 0.304 | 0.110 | 0.064

## Slide 21: GPS-levelling comparisons (3)
Geoid – mod 90 with Faye-Helmert | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.533 | 0.075 | 0.037
New Finnish GPS | 0.407 | 0.046 | 0.045
”Torge” | 0.338 | 0.221 | 0.070
SWET | 0.354 | 0.083 | 0.041
Baltic sea level | 0.458 | 0.108 | 0.080
REFDK | 0.100 | 0.058 | 0.031
Sognefjord | 0.527 | 0.080 | 0.060
New Norway GPS | 0.368 | 0.101 | 0.059
NKG96 geoid Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | 0.188 | 0.086 | 0.051
New Finnish GPS | 0.119 | 0.074 | 0.049
”Torge” | 0.016 | 0.097 | 0.045
SWET | -0.001 | 0.118 | 0.065
Baltic sea level | 0.101 | 0.094 | 0.068
REFDK | -0.148 | 0.023 | 0.020
Sognefjord | 0.121 | 0.065 | 0.061
New Norway GPS | -0.053 | 0.153 | 0.072

## Slide 22: GPS-levelling comparisons (4)
GOCINA/OCTAS Aug 2004 geoid Unit: m | Mean | Std.dev. | Std.dev. after 4-par fit
New Sweden GPS | -0.409 | 0.079 | 0.036
New Finnish GPS | -0.549 | 0.045 | 0.042
”Torge” | -0.560 | 0.191 | 0.065
SWET | -0.602 | 0.087 | 0.042
Baltic sea level | -0.488 | 0.101 | 0.070
REFDK | -0.843 | 0.053 | 0.025
Sognefjord | -0.358 | 0.087 | 0.054
New Norway GPS | -0.589 | 0.109 | 0.052
GOCINA/OCTAS geoid is covering the entire North Atlantic region (from Greenland to Urals).
Resolution of basic grid is 5 km. Computed as a classical geoid by Helmert condensation.
Marine gravity data adjusted in the North Atlantic. A. Olesen / R. Forsberg, Aug. 2004.

## Slide 23: Geoid difference (geoid30 – NKG96)

## Slide 24: KMS03 altimetry – geoid30

## Slide 25: Geoid fit to REFDK - Denmark

## Slide 26: Geoid fit to REFDK - Sweden

## Slide 27: Conclusions
New geoid: NKG2004 = geoid30.gri + 35 cm
Incorporates much new data relative to NKG96 - Baltic Sea airborne - New Sedish and Norwegian data - Russia - Baltic states - New DEM - GRACE GGM02S
Better fit than NKG96, slightly better than GOCINA/OCTAS (except in Norway)
NKG2004 fitted to be ”approximately” at UELN heights
Fit to national systems: ”fitgeoid.job”