## Slide 1: The NKG2015 gravimetric geoid model for the Nordic-Baltic region
J. Ågren, G. Strykowski, M. Bilker-Koivula, O. Omang, S. Märdla, R. Forsberg, A. Ellmann, T. Oja, I. Liepins, E. Parseliunas, J. Kaminskis, L.E. Sjöberg, G. Valsson

## Slide 2: Background
The Nordic Geodetic Commission (NKG) is an association of geodesists from Denmark, Finland, Iceland, Norway and Sweden.
The purpose of NKG is mutual exchange, cooperation and coordination of work with the geodetic infrastructure in the region.
The Baltic countries Estonia, Latvia and Lithuania also take a very active part in the work.
During the years, NKG has computed several gravimetric geoid models:
  NKG1986 (Tscherning and Forsberg 1986)
  NKG1989 (Forsberg 1990)
  NKG1996 (Forsberg et al. 1996)
  NKG2002
  NKG2004
These NKG models have been used as a basis to construct national height corrections models.

## Slide 3
Introduction
The NKG2015 geoid model project started in 2011 with the goal to compute the next official NKG (quasi)geoid model in Nordic and Baltic cooperation
The project has consisted of the following parts:
  Specification (what to do, definitions/conventions on reference systems, as far as possible common reference systems/frames, zero permanent tide, postglacial land uplift epoch 2000)
  Data updates (gravity database, DEM, GNSS/levelling, Ice thickness model)
  Computation (five computation centres, additional gridding investigations)
  Publication (on-going)
The final NKG2015 model is hereby released.
The main purpose of this paper is to present the project and the computations that led to the new NKG2015 geoid model.
The model is compared with some other models available over the region.

## Slide 4: NKG gravity database
Responsible: Gabriel Strykowski, DTU Space.
Has been modernised and is now implemented in PostgrSQL with both a line-based and web-based interface, but still using the same 80-character format as before.
Horizontal positions and heights transformed to national ETRS 89 and EVRS realisations.
Updated with quality checked and new data from all the Nordic and Baltic countries.
Data transformed to zero permanent tide system and epoch 2000.0 (if meaningful).
Version 4 delivered June 18, 2016

## Slide 5: GNSS/levelling database
Responsible: Ove Omang, Jonas Ågren, Pasi Häkli (transformations)
Levelled heights both in national EVRS realisations and in EVRF 2007.
The GNSS-heights have been transformed to the common ETRS 89 realisation ETRF2000 epoch 2000.0 using the so-called NKG2008 transformations (Häkli et al. 2016).
These transformations consist of a 7-parameter part and a postglacial land uplift correction part (NKG2005LU).
Version 3 confirmed in early 2016 with the publication of Häkli et al. (2016).

## Slide 6
Evaluation of regional geoid computation methods, strategies and software (“The NKG pageant contest” )
Five computations centres:
    Lantmäteriet (LM) - Jonas Ågren
    Tallinn Technical University/Estonian Land Board (TTU/ELB)- Silja Märdla, Artu Ellmann and Tõnis Oja
    DTU Space (DTU) - René Forsberg and Gabriel Strykowski
    National Land Survey of Finland - Finnish Geospatial Research Institute (NLS-FGI) - Mirjam Bilker-Koivula
    Norwegian Mapping Authority (NMA) - Ove Omang
The task: compute a gravimetric quasigeoid model in the epoch 2000.0 and zero tide system using the above data.
It was specified that the following GGMs can be used (converted to the zero tide system),
  GO_CONS_GCF_2_DIR_R5 (Bruinsma et al, 2013)
  EIGEN-6C4 (Förste et al, 2014)
(Tests have been made later on with GOCO05S)
The choice of final computation method (#1a; see next slide) was based mainly on the fit to GNSS/levelling.

## Slide 7
Results from the GNSS/levelling 1-parameter fits

## Slide 8: Method used for the final gravimetric model
LSMSA or KTH-method (Sjöberg 1991, 2003,…).
The height anomaly is computed as
  Least squares (stochastic) kernel modification (Sjöberg 1991,…).
Surface gravity anomalies gridded using a Remove-Interpolate-Restore technique, in which
  the gridding was made on the reduced gravity anomaly (reduced for the GGM, RTM, ATM and ICE effects)
  using Least Square Collocation (Geogrid) with individual a priori standard errors for the observation errors (except in Norway where constant 0.5 mGal a priori standard errors are used as is recommended by Märdla et al. 2016). Correlation length 15 km.
Stokes’ integral evaluated using spherical 1D FFT (Haagmans et al. 1993)

## Slide 9
GNSS/levelling residuals for the final gravimetric model after a 1-parameter fit/transformation
# | Min | Max | Mean | StdDev
2538 | -0.1740 | 0.1740 | 0.0000 | 0.0285
Normal heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations transformed to ETRF2000 epoch 2000.0 and zero tide system.

## Slide 10
The above gravimetric model is fitted to ETRF2000 epoch 2000.0 and the National EVRS realisations using a 1-parameter transformation.
In order to be able to use the NKG2015 model directly for height determination with GNSS, a permanent tide system correction is included for the GNSS-heights. The following observation equation is used:
which gives the final NKG2015 model:
The gravimetric character of the model is preserved, which means that it is easy for each country to adopt it to GNSS/levelling as they prefer.
Since the above permanent tide correction is included, some would call this a height correction model.
Computation of the final NKG2015 model

## Slide 11: Comparison with other quasigeoid models available over the whole Nordic/Baltic region

## Slide 12
GNSS/levelling residuals for EIGEN-6C4 after a 1-parameter fit/transformation
# | Min | Max | Mean | StdDev
2538 | -0.2340 | 0.1950 | 0.0000 | 0.0421
Normal heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations transformed to ETRF2000 epoch 2000.0, converted to the zero permanent tide.

## Slide 13: Difference between NKG2015 and EIGEN-6C4
Correction to the same permanent tide system, mean removed.
Contour intervals: 2 cm for whole area (1 cm in Norway close up).
It is clear that the omission error (above degree 2190) is very significant in Norway.
There are large data dependent differences in some areas, mainly east of Finland and in the Gulf of Finland; see Bilker-Koivula (2015).

## Slide 14: Conclusions
The final NKG2015 geoid model is hereby released.
It has been computed in Nordic/Baltic co-operation in a long term project under the umbrella of NKG (Nordic Geodetic Commission).
The final gravimetric model is computed using the LSMSA method.
The standard deviation in the 1-parameter fit to GNSS/levelling is 2.85 cm, which is significantly better than for previous models.
In sub-areas (countries) with a smooth gravity field, the fit standard deviation is considerably lower, around 1.5-2.0 cm.
The NKG2015 geoid model will now be used as a basis to compute national height correction models, for instance in Sweden.
Since the final model has been fitted to GNSS/levelling with a 1-parameter transformation, and since it also includes a correction between the zero and non-tidal permanent tide systems, it is also directly usable for GNSS height determination.
This is not the end of geoid determination in the NKG area: Right now the main focus is on the Baltic Sea geoid in the EU project FAMOS, for which the NKG2015 will be used as initial reference model (to be checked and improved).